## Slide 1: Data-Driven Neural Network Modeling of Nonlinear Fluid Dynamic Systems
Supervisor: Prof. Ashoke De Department of Aerospace Engineering, IIT Kanpur
Team Members: Aman Kashyap, Atharv Soni, Aditya Yadav, Prabal Pratap Singh

## Slide 2: Table of Contents
Problem Statement 3
Motivation 4
Introduction 5
Airfoil Selection 9
High-Fidelity Data Generation 13
Data Preprocessing 15
Surrogate Model & PINNs 16
Neural Network Architecture 18
Training & Setup 20
Results & Observations 21
Computational Speedup 23
Learnings 28
Future Work 29
Q&A 30
References 31
Team Contributions 32

## Slide 3: Problem Statement
Aerodynamic analysis is critical in fluid dynamics research, especially for aerospace applications. However, traditional Computational Fluid Dynamics (CFD) methods, like Navier-Stokes solvers, are computationally intensive and time-consuming.
This limits scalability for real-time simulations, iterative design processes, and large-scale optimization.
To address this bottleneck, we aim to develop a neural network-based surrogate model that:
    Accurately captures nonlinear and transient aerodynamic behavior
    Achieves CFD-level accuracy
    Requires significantly less computational time and resources
By training on data from high-fidelity Navier-Stokes simulations, the model learns to emulate complex flow dynamics—enabling fast, reliable predictions without re-running expensive CFD simulations.

## Slide 4: Motivation
Real-time analysis for autonomous systems, UAVs, optimization loops.
Limitations of existing CFD solvers (XFOIL, FLOW-Unsteady) in speed.
Recent advances in ML enable physics-consistent fast approximations.
PINNs offer a bridge between purely data-driven models and physically accurate simulations.

## Slide 5: Introduction
Aerodynamic analysis traditionally relies on CFD simulations.
High-fidelity methods are computationally intensive and time-consuming.
The need: fast, accurate, and physically consistent surrogate models.
Our approach: Physics-Informed Neural Networks (PINNs) for surrogate aerodynamic prediction.

## Slide 6: What is CFD?
Computational Fluid Dynamics (CFD) is the use of numerical methods to solve fluid flow equations — primarily the Navier-Stokes equations.
CFD enables simulation of airflows over wings, cars, turbines, etc.
Requires:
  Discretization of the flow domain (meshing).
  Solving large systems of nonlinear PDEs iteratively.
Tools used in this project:
  XFOIL – lightweight 2D panel method, fast but limited near stall.
  FLOW-Unsteady – high-fidelity Navier-Stokes solver with turbulence modeling.
While accurate, CFD simulations are time-consuming — especially for unsteady or 3D problems.

## Slide 7: The Navier-Stokes Equations
“The governing equations of fluid motion”
Momentum Equation (Incompressible Navier-Stokes):
  ρ: Density
  u: Velocity vector
  p: Pressure
  μ: Viscosity
Continuity Equation (Mass conservation):
These nonlinear partial differential equations are computationally intensive to solve, especially for:
  High Reynolds number flows
  Turbulence and separation
  Time-varying (transient) regimes

## Slide 8
8

## Slide 9: Airfoil Selection
~100 airfoils selected through web-based aerodynamic databases, research literature, and curated lists to ensure geometric and performance diversity.
NACA series (e.g., 0012)
Modern laminar flow profiles.
Covered diverse aerodynamic behavior across:
Cambered/symmetric
Low/high Re
Thin/thick profiles.

## Slide 10: Airfoil Characteristics and Diversity
10
Diversity in dataset ensures generalization of the neural network.
Key aspects:
  Lift and drag behavior variation.
  Stall characteristics captured.
  Variety in thickness-to-chord ratios.
Broader feature space => Better ML model performance.

## Slide 11: Baseline Simulations using XFOIL
Simulations at Reynolds numbers: 3317, 13131, 22978, 28404, 41039, 44913.
Angles of Attack: −20° to +20°.
Output:
  Cl (Lift coefficient)
  Cd (Drag coefficient)
  Cm (Moment coefficient)
Used for both training and benchmarking.
Figure 1: Paneling of the NACA 3410 airfoil in XFOIL showing 160 panel nodes with a max panel angle of 9.88°. Accurate paneling is crucial for resolving surface pressure distribution.

## Slide 12: Why XFOIL?
Fast and lightweight CFD solver.
Suitable for bulk data generation.
Limitations acknowledged:
Struggles with strong separation, high turbulence.
Balanced by high-fidelity FLOW-Unsteady simulations.

## Slide 13: High-Fidelity Data Generation
Used FLOW-Unsteady solver from BYU labs.
Simulated:
  Velocity fields
  Pressure fields
  Vorticity structures
Provided physically accurate training data.
Figure 2: Pressure coefficient distribution and aerodynamic polar output for NACA 3410 at various angles of attack, computed using XFOIL at Re = 0.013 × 10⁶.

## Slide 14
Sample XFOIL Data (Re = 13131)
The following table presents a subset of the aerodynamic data generated using XFOIL for the NACA 2508 airfoil at a Reynolds number of 13,131. Each row corresponds to a different angle of attack (AoA), and includes coefficients for lift (Cl), drag (Cd), pressure drag (Cdp), and moment (Cm), along with transition locations (TopXtr and BotXtr).
alpha | CL | CD | CDp | CM | TopXtr | BotXtr
-14.00000 | -0.37440 | 0.16238 | 0.14894 | 0.01280 | 1.00000 | 0.68540
-13.00000 | -0.33360 | 0.14875 | 0.13521 | 0.01010 | 1.00000 | 0.78890
-12.00000 | -0.37100 | 0.13379 | 0.11839 | 0.01150 | 1.00000 | 1.00000
-11.00000 | -0.33370 | 0.12041 | 0.10496 | 0.00600 | 1.00000 | 1.00000
-10.00000 | -0.29710 | 0.10725 | 0.09176 | 0.00080 | 1.00000 | 1.00000
-9.00000 | -0.26100 | 0.09443 | 0.07884 | -0.00430 | 1.00000 | 1.00000
-8.00000 | -0.29370 | 0.09070 | 0.07545 | 0.00680 | 1.00000 | 0.93070
-7.00000 | -0.41300 | 0.09283 | 0.07857 | 0.01680 | 1.00000 | 0.64290
-6.00000 | -0.44450 | 0.08203 | 0.06841 | 0.01230 | 1.00000 | 0.55250
-5.00000 | -0.44890 | 0.06833 | 0.05509 | 0.00630 | 1.00000 | 0.52880

## Slide 15: Data Preprocessing
Normalization:
  Min-max scaling of inputs (Re, AoA, spatial coords).
Feature engineering:
  Added Cp (pressure coefficient) as a derived parameter.
Outlier removal:
  IQR filtering to clean anomalies.
Final structured dataset prepared for neural network ingestion.

## Slide 16: What is a Surrogate Model?
Fast approximation of a computationally expensive simulator.
Learns to emulate input-output behavior.
In our case: PINN predicts Cl, Cd, Cm based on Re, AoA, geometry.
Key advantage: Speed without losing physics.

## Slide 17: Why We Need Surrogate Models
Solving Navier-Stokes equations via CFD is:
  Accurate, but
  Slow and computationally expensive
Example: A full CFD run may take hours per case, making design sweeps and real-time applications infeasible.
Surrogate Model Solution:
  Learn the aerodynamic behavior from CFD data.
  Retain physical accuracy by embedding physics into the neural network (PINN).
  Predict Cl, Cd, Cm in milliseconds — enabling rapid analysis, control systems, and optimization.
Our goal: "Match CFD accuracy while reducing computation time by 100x–300x."

## Slide 18: Neural Network Architecture
Two-stage architecture:
NavierStokesPINN: Predicts flow field (u, v, p).
AerodynamicsPINN: Predicts aerodynamic coefficients.
Physics-informed loss:
Combines MSE loss + Navier-Stokes residuals.
Activation: Tanh; Optimizer: Adam; Regularization: Dropout 0.2.
Figure 3: Model Architecture of the Dual-Stage Physics-Informed Neural Network (PINN)

## Slide 19: Loss Function Design
Total Loss = Data Loss + λ × Physics Residual Loss.
Ensures:
  Data-driven learning
  Respect for conservation laws.
  Reduces unphysical predictions outside the training range.

## Slide 20: Training Setup
Learning rate: 0.001 with decay.
Batch size: 256.
500 epochs with early stopping.
Computation done on Param Sanganak (NSM Facility).
Used 3×48 core nodes for efficient parallelization.

## Slide 21: Results – Steady-State Accuracy
Cl prediction:
  MAE: 5.2%
  R²: 0.91
Cd prediction:
  MAE: 7.8%
  R²: 0.87
Good agreement with XFOIL results at positive AoA.
Aerodynamic Coefficient | Mean Absolute Error (MAE) | R² Score
Lift Coefficient (Cl) | 5.2% | 0.91
Drag Coefficient (Cd) | 7.8% | 0.87

## Slide 22: Results – Transient Regime Challenges
In stall and separation zones (AoA < 0°):
  MAE increased to 15–20%.
Complex flow physics harder for the PINN to capture.
Future directions: LSTM-based temporal modeling.

## Slide 23: Computational Speedup
Surrogate drastically reduces analysis time — makes real-time feasible.
Simulation Tool | Avg. Time per Case | Total Time (15k Cases) | Hardware | Speedup
XFOIL | 4 minutes | ~1000 hours | Single Core | 1×
PINN | 0.8 seconds | ~3.3 hours | 3×48 Core HPC | 300×

## Slide 24: Visual Comparisons
Plots:
  True vs Predicted Cl, Cd
  True vs Predicted η
  True vs Predicted Cq
Steady-state regions: Good match
Stall regions: Deviations exist but trends captured
PINN demonstrates potential with minor refinements.

## Slide 25
Key Observations:
Initial Gap: Predicted CT values differ notably from true values early on, revealing model limitations.
Refinement Path: Errors guided improvements like data augmentation and retraining.
Progress Baseline: Plot acts as a benchmark to evaluate future optimizations.
Clear Visualization: Original-scale comparison highlights model shortcomings and areas for tuning.
25

## Slide 26
Key Observations (η Plot):
Initial Dip in True η: A steep decline followed by recovery reflects transient aerodynamic effects before stabilization.
Prediction Oscillations: Predicted η remains stable but oscillatory, indicating limited capture of early transients.
Better Steady-State Match: Model performance improves significantly in later samples, aligning well under steady conditions.
26

## Slide 27
Key Observations (Cq):
Transient Phase: True Cq values show sharp variation early on, reflecting transient flow dynamics.
Model Bias: Predicted Cq remains smoother but oscillates, revealing limited capture of early non-linear effects.
Steady-State Accuracy: Alignment improves over time, indicating better model reliability in later, stable regimes.
27

## Slide 28: Learnings and Key Takeaways
ML models can emulate aerodynamic behavior with high speed and reasonable accuracy.
Embedding physics dramatically improves generalization.
Dataset diversity is critical.
Flow separation remains a challenge without temporal memory (LSTM, RNN).

## Slide 29: Future Work
Extend model to 3D wings and full aircraft sections.
Incorporate experimental datasets for validation.
Develop uncertainty quantification around predictions.
Explore hybrid ML-CFD pipelines for complex flow regimes.

## Slide 30: Thank You
We thank the National Supercomputing Mission for HPC access and Prof. Ashoke De for his valuable mentorship.
We welcome any questions from the panel.

## Slide 31: Team Contributions
Aman Kashyap
Airfoil Selection & Baseline Simulation (XFOIL) Generated baseline aerodynamic data for 100+ airfoils using XFOIL and supported neural network training on Param Sanganak.
Aditya Yadav
Data Preprocessing & Feature Engineering
Normalized and structured the simulation data, filtered outliers, and derived essential flow parameters for neural network input.
Prabal Pratap Singh
Neural Network Design, Training & Validation
Developed and trained a two-stage PINN architecture, handled performance benchmarking, and integrated physics-informed loss design.
Atharv Soni
High-Fidelity Data Generation (FLOW-Unsteady)
Performed advanced CFD simulations using FLOW-Unsteady with turbulence modeling to generate physically rich data for ML training.

## Slide 32: References
Alvarez, E. J., Mehr, J., & Ning, A. (2022). FLOWUnsteady: An Interactional Aerodynamics Solver for Multirotor Aircraft and Wind Energy. AIAA Aviation Forum, Chicago, IL, June 2022.
Raissi, M., Perdikaris, P., & Karniadakis, G. E. (2019). Physics-Informed Neural Networks: A Deep Learning Framework for Solving Forward and Inverse Problems Involving Nonlinear Partial Differential Equations. Journal of Computational Physics, 378, 686–707.
Zhang, D., Lu, L., Guo, L., & Karniadakis, G. E. (2019). Quantifying Total Uncertainty in Physics-Informed Neural Networks for Solving Forward and Inverse Stochastic Problems. Journal of Computational Physics, 397, 108850.
Chakraborty, S., & Karniadakis, G. E. (2021). Transfer Learning Based Multi-Fidelity Physics-Informed Deep Neural Network. Journal of Computational Physics, 426, 109942.
Liu, X., Zhang, X., Peng, W., Zhou, W., & Yao, W. (2022). A Novel Meta-Learning Initialization Method for Physics-Informed Neural Networks. Neural Computing and Applications, 34(17), 14511–14534.